## Slide 1
AIORI 3 Level 1 proposal
A3-PS033-TC378 8 October 2026
1 / 11
A3-PS033-TC378
DNS-Based Discovery
of Diagnostic Services
Chris Itty Biju and Alan Jayan Joseph
Faculty mentor: Revathi BS
Karunya University of Technology and Sciences
Notes: Introduce the team: Chris Itty Biju and Alan Jayan Joseph, guided by Revathi BS, Karunya University of Technology and Sciences. This is PS-033 in Cloud Computing and IoT. The proposal focuses on discovering diagnostic services through signed DNS metadata. Source: supplied PS-033.pdf and organizer presentation structure.

## Slide 2
Problem Description
AIORI 3 Abstract
A3-PS033-TC378 8 October 2026
2 / 11
Changing service locations
Hardcoded IP addresses and ports become outdated when diagnostic endpoints move.
Unverified connection details
The client needs to detect altered DNS data and reject metadata it cannot interpret.
Proposed approach
Discover service details through signed DNS records, then authenticate before invocation.
Notes: A program that stores a diagnostic endpoint as a fixed IP and port can fail when that endpoint moves. Our solution lets it discover connection details through DNS. We then verify the published metadata and authenticate separately before use. The scope is one lab zone, three mock diagnostic services and one client. This is the scope in PS-033.pdf.

## Slide 3
Background
AIORI 3 Background
A3-PS033-TC378 8 October 2026
3 / 11
DNS and SVCB
Find the service hostname, port and capability metadata.
DNSSEC
Check the origin and integrity of the published DNS records.
TLS and service credentials
Verify the endpoint identity and the caller's permission.
Valid DNS metadata alone grants no service access.
Notes: DNS is the directory. SVCB is the record format used to publish connection parameters. DNSSEC verifies signed records against a trust anchor. TLS verifies the endpoint identity and protects the connection. A service token gives the caller access to a permitted operation. These checks have different jobs. Authentic metadata does not prove that a service is trustworthy or authorize a call. Sources: https://datatracker.ietf.org/doc/html/draft-mozleywilliams-dnsop-dnsaid-02; https://www.rfc-editor.org/rfc/rfc9460.html; https://www.rfc-editor.org/rfc/rfc4033.

## Slide 4
Literature & RFC Review
AIORI 3 Literature & RFC Review
A3-PS033-TC378 8 October 2026
4 / 11
DNS-AID draft -02
Pinned proposal for known-service discovery and security boundaries. Work in progress.
RFC 9460
SVCB ServiceMode records carry connection parameters and mandatory metadata keys.
RFC 4033, RFC 4034 and RFC 4035
DNSSEC requirements, signed record formats and validation procedures.
Notes: The proposed pin is draft-mozleywilliams-dnsop-dnsaid-02, dated 27 May 2026. It is an individual Internet-Draft and remains work in progress. Section 3.1 covers known-agent discovery and section 6 discusses security. RFC 9460 specifies SVCB. RFCs 4033, 4034 and 4035 describe DNSSEC. The lab uses local private-use keys for capability and invocation path; these are documented extensions, not assigned DNS-AID parameter numbers. References: https://datatracker.ietf.org/doc/html/draft-mozleywilliams-dnsop-dnsaid-02; https://www.rfc-editor.org/rfc/rfc9460.html; https://www.rfc-editor.org/rfc/rfc4034; https://www.rfc-editor.org/rfc/rfc4035.

## Slide 5
Proposed Solution
AIORI 3 Proposed Solution
A3-PS033-TC378 8 October 2026
5 / 11
One signed test zone
A publisher advertises service connection details in diag.test using SVCB and address records.
Three mock diagnostic services
Latency, traceroute and health services return clearly labelled sample results.
One discovery and invocation client
The client validates DNSSEC, metadata and TLS before sending a service-specific token.
Local prototype: real security checks, simulated diagnostic measurements.
Notes: The publisher generates and signs a diag.test zone. Three services represent latency, traceroute and system health. The client verifies SVCB and address signatures, checks the metadata, verifies TLS and uses a per-service credential. The existing local prototype uses real DNS, DNSSEC, TLS and HTTP. Its diagnostic outputs are fixtures, labelled mock. It uses a locally provisioned trust anchor, not a public DNS root chain. Source: current lab.py and docs/PROTOCOL.md in this project.

## Slide 6
Optimization Proposed
AIORI 3 Solution Optimization
A3-PS033-TC378 8 October 2026
6 / 11
Area | Manually configured setup | Proposed discovery workflow
Endpoint change | Update each stored endpoint | Publish new signed connection details
Metadata integrity | No signature check by default | Reject invalid or unsigned DNS answers
Access control | Credentials configured separately | Keep credentials separate from discovery
Repeated lookups | No discovery cache involved | Evaluate TTL-aware caching later
Port migration already works in the lab. Caching and performance gains remain to be evaluated.
Notes: The comparison describes expected behavior, not measured speed improvements. The current demo changes service ports through the publisher without changing discovery-client code. Signature failures and malformed metadata produce different errors. Credentials remain separate from discovery. TTL-aware caching is proposed future work; we will measure cold and warm lookup times after implementing it. Sources: PS-033.pdf, current lab.py and project protocol document.

## Slide 7
Solution Architecture & Design
AIORI 3 Architecture Design (UML)
A3-PS033-TC378 8 October 2026
7 / 11
<<component>>
Publisher
<<component>>
Signed DNS zone
<<component>>
Discovery client
publishes
queries
<<component>>
Three mock services
TLS + token
Independent local provisioning
Client: DNS / TLS trust and service token.
Services: credential verification settings.
DNS integrity, endpoint identity and service access remain separate checks.
Notes: This component diagram shows dependencies. The publisher writes a signed zone served by the DNS listener. The discovery client queries that listener and validates records. Local provisioning provides the public DNS trust anchor, TLS trust material and service credentials through separate configuration. After the checks, the client invokes three separate mock service listeners. The initial implementation shares one laptop; later deployment can separate the components. DNS signing private keys stay with the publisher and are not sent to the client. Source: project implementation and PS-033.pdf.

## Slide 8
Data Flow Diagram
AIORI 3 Data Flow Diagram
A3-PS033-TC378 8 October 2026
8 / 11
1. Query DNS
2. Check signatures
and metadata
3. Validate service
address record
6. Return mock result
5. Check caller token
4. Verify TLS identity
Signed SVCB metadata
Signed A record
Invalid signatures or metadata stop discovery.
Connection failures or rejected credentials stop invocation.
Notes: Start from a known logical service name. Query SVCB, verify the signature and metadata, then query and verify the address record. Only after these checks does the client connect through TLS and present a token. The service authenticates the caller and returns a mock result. Failures stop the flow at their respective stage. Bogus signatures are different from correctly signed but malformed metadata. Missing service listeners and wrong credentials are additional negative cases. Source: lab.py and PS-033.pdf.

## Slide 9
Deployment Timeline
AIORI 3 Deployment Timeline
A3-PS033-TC378 8 October 2026
9 / 11
8-10 October: preparation
Review scope with the mentor, finalize the proposal and resolve the GitHub setup questions.
11-13 October: Level 1 materials
Record each member, upload the PDF and video link, and confirm repository access and transfer.
14 October: Level 1 deadline
Complete steps 1-7. During 16-31 October, continue mentoring, code and demo delivery.
13 October is our suggested readiness target, not an organizer-issued deadline.
Notes: The dates 14 October and 16-31 October come from the organizer guidelines. We target 13 October internally for readiness, because the page does not give an exact cutoff time. The local starter exists. We will use the preparation phase for team understanding, slides, video, and GitHub coordination. Later mentoring focuses on deployment separation and evaluation. Source: https://portal.aiori.in/aiori-3/hackathon-guideline/.

## Slide 10
Bibliography
AIORI 3 Bibliography
A3-PS033-TC378 8 October 2026
10 / 11
[1] DNS-AID draft -02
Mozley et al., 27 May 2026. Individual Internet-Draft.
[2] RFC 9460
Service Binding and Parameter Specification via the DNS.
[3] RFC 4033, RFC 4034 and RFC 4035
DNSSEC requirements, resource records and protocol changes.
[4] AIORI-3 organizer materials
PS-033, presentation structure and online hackathon guidelines.
Draft ID: draft-mozleywilliams-dnsop-dnsaid-02
Notes: Full references: DNS-AID -02: https://datatracker.ietf.org/doc/html/draft-mozleywilliams-dnsop-dnsaid-02
RFC 9460: https://www.rfc-editor.org/rfc/rfc9460.html
RFC 4033: https://www.rfc-editor.org/rfc/rfc4033
RFC 4034: https://www.rfc-editor.org/rfc/rfc4034
RFC 4035: https://www.rfc-editor.org/rfc/rfc4035
Official guidelines: https://portal.aiori.in/aiori-3/hackathon-guideline/
Local sources: PS-033.pdf and Proposed-structure-hackathon.pdf supplied by the team.

## Slide 11
Thank You
AIORI 3 Questions
A3-PS033-TC378 8 October 2026
11 / 11
A3-PS033-TC378
One signed zone. Three mock services.
A client that checks before it invokes.
Chris Itty Biju and Alan Jayan Joseph
Faculty mentor: Revathi BS
Notes: Close with the project goal: discover diagnostic services dynamically while keeping metadata integrity and service access separate. Proposed responsibilities: Chris focuses on DNS publication and validation, Alan on the client and mock services, and Revathi BS on review and mentoring. These roles are suggestions to confirm before recording. Invite questions about why DNSSEC does not grant authorization.